How many bits would it take to implement a full page table for this virtual memory scheme?
The original design:
- 32 bit virtual memory address
- 32 bit physical memory address.
- Using a 4096 bytes (4 Kib) page size, each physical page number consists of 20 bits.
  Assumption:
- Physical addresses are small enough to fit in the same number of bits as physical memory address (32-bits).
- Every virtual page number needs a corresponding page table entry (PTE).
  Include:
- valid bits
- dirty bits
- reference bits
- the space for physical/disk addresses in your calculation (as illustrated in Figure 5.29).

Page Table = 2^(address space size – page size) * PTE (byte)
full page table: 232 x 2-12 x 2
4MB
How many bits would it take to implement a full page table for this virtual memory scheme?
The original design:
- 32 bit virtual memory address
- 32 bit physical memory address.
- Using a 8192 bytes (8 Kib) page size, each physical page number consists of 19 bits.
Assumption:
- Physical addresses are small enough to fit in the same number of bits as physical memory address (32-bits).
- Every virtual page number needs a corresponding page table entry (PTE).
Include:
- valid bits
- dirty bits
- reference bits
- the space for physical/disk addresses in your calculation
1. C(++) program to implement calculation for implementing a Full Page Table for Virtual memory from 1 and 2.
  1. Assumption: disk addresses require the same number of bits as physical memory addresses.
  2. Output: # of bits that would be required to implement the full page table.